## Slide 1
Power Electronics and Control Engineering (PEACE) Laboratory
Parametric uncertainty estimation-based adaptive loss optimization in
DAB dc-dc converter
1
Sanat Agrawal
June 14, 2024

## Slide 2
Power Electronics and Control Engineering (PEACE) Laboratory
2
Background of the DAB Converter Topology
Applications:
  for battery systems, renewable energy, solid-state transformers, and low- to medium-voltage grid applications.
  Such as distributed renewable energy systems (PV or wind, residential loads, battery storage), EV charging (dc or ac grid, HV battery, LV battery/vehicle load), space power supply
Project Target:
  Estimation of various Parameters of DAB
  Optimize the Power loss by using the estimated parameter and predicting optimal point of operation

## Slide 3
Power Electronics and Control Engineering (PEACE) Laboratory
3
Background of the DAB Converter Topology
Equivalent Lossless model

## Slide 4
Power Electronics and Control Engineering (PEACE) Laboratory
4
DAB Modeling
Frequency Domain
Time Domain
Power out in SPS control
Output Power Derivation using Lossless Models

## Slide 5
Power Electronics and Control Engineering (PEACE) Laboratory
5
Problems in current scenario
Solving Various Power Loss equations to get a optimal Operating point
  Assumption that the converters
L,C s are constant
and does not change with time
2. All Losses cant be modelled accurately

## Slide 6
Power Electronics and Control Engineering (PEACE) Laboratory
6
A Possible Solution
Using Machine Learning for parametric estimation
ML based adaptive loss optimization

## Slide 7
Power Electronics and Control Engineering (PEACE) Laboratory
6
Machine Learning
Outputs
  L
  Rds
  C
ML MODEL
Inputs
  Phi
  current(I1,I2)
  Voltage(V1,V2)
Ways of Data Collection:-
  Hardware Setup
  Simulation Model
  Mathematical solution

## Slide 8
Power Electronics and Control Engineering (PEACE) Laboratory
6
COMPARISON OF SETUPS
Simulation Model
Method
Hardware Setup
Pros
Cons
Mathematical solution
Accurate values of V,I,L
Some what
Accurate values
changing L -> Huge time
Varying all parameter
will take days of time
Less Accurate as Losses
are not Modelled
Faster Data
Collection

## Slide 9
DAB model in MATLAB
Power Electronics and Control Engineering (PEACE) Laboratory
6
MATLAB MODEL
DATA Collection
ML MODEL
Estimated L value

## Slide 10
Power Electronics and Control Engineering (PEACE) Laboratory
6
MATLAB MODEL
DATA Collection No.
  L ( +-5% in steps of 1%) 11
  Phi(0 to 1.5 in steps of 0.07) 21
Total = 21*11= 231 data
ML MODEL
  Phi
  current(I1,I2)
  Voltage(V1,V2)
L

## Slide 11
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL - 1 (LINEAR REGRESSION)
Average Error :
1.16%

## Slide 12
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL - 2 (POLYNOMIAL REGRESSION)
Degree 5 Polynomial
Average Error :
0.69%

## Slide 13
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL - 3 (Neural Network)

## Slide 14
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL - 3 (Neural Network)
Average Error :
2.48%

## Slide 15
 | 1.16% | 
 | 0.69% | 
 | 2.48% | 
Power Electronics and Control Engineering (PEACE) Laboratory
6
COMPARISON OF MODELS
1.Linear Regression
2.Polynomial Regression
3. Simple Neural Network

## Slide 16
Power Electronics and Control Engineering (PEACE) Laboratory
6
PROBLEMS FACED
  Very Slow DATA Collection i.e (230 points in ~ 4hr)
2. Simple Models gives good results due to lack of data
Solution
  Using other software for DATA collection (PLECS with parallel computing )
6000 points in ~ 3 hr
2. USE of Other Models with Bigger DATA
3. Less data leads to Poor training of Model

## Slide 17
DAB model in PLECS
Power Electronics and Control Engineering (PEACE) Laboratory
6
PLECS MODEL
DATA Collection
via Parallelization
ML MODEL
Estimated L value

## Slide 18
Power Electronics and Control Engineering (PEACE) Laboratory
6
PLECS MODEL
DATA Collection No.
  L ( +-20% in steps of 0.2%) 201
  Phi(0 to 1.5 in steps of 0.05) 31
Total = 201*31= 6231 data
ML MODEL
  Phi
  current(I1,I2)
  Voltage(V1,V2)
L

## Slide 19
Power Electronics and Control Engineering (PEACE) Laboratory
6
DECISION TREE

## Slide 20
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -1 (RANDOM FOREST )
RANDOM FOREST
A TREE
1. Prone To overfitting
2. Poor Generalization

## Slide 21
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -1 (RANDOM FOREST )
0.33%

## Slide 22
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -1 (RANDOM FOREST )
L(Analytic) should be
greater than
L(Actual & Prediction)
Lossless
Average: 3%

## Slide 23
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -1 (RANDOM FOREST )
L vs POWER
Phi Variation
Power increases with increase in Phi for a fixed L
0.1 to 1.5

## Slide 24
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -1 (RANDOM FOREST )
L vs POWER
Phi Variation
Power increases with increase in Phi for a fixed L
0.1 to 1.5

## Slide 25
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -1 (RANDOM FOREST )
L vs POWER
Phi Variation
Power increases with increase in Phi for a fixed L
0.1 to 1.5

## Slide 26
Power Electronics and Control Engineering (PEACE) Laboratory
6
FURTHER PLANS
=>Collect data with more parameters(deltas)
using simulation and mathematical models
=>Using Physics constraints as loss in MODEL
=> Find a model which require Less data
and gives satisfactory results

## Slide 27
Power Electronics and Control Engineering (PEACE) Laboratory
6
PLECS MODEL
DATA Collection No.
  L ( +-20% in steps of 0.8%) 51
  Phi(0 to 1.5 in steps of 0.1) 16
  del1 (0 to 1.4 in steps of 0.2) 8
  del2 (0 to 1.4 in steps of 0.2) 8
Total = 51*16*8*8= 27000 data

## Slide 28
Power Electronics and Control Engineering (PEACE) Laboratory
6
DERIVED FEATURE
L_Analytical
loss

## Slide 29
Power Electronics and Control Engineering (PEACE) Laboratory
6
ML MODEL
ML MODEL
  Phi,del1,del2
  current(I1,I2)
  Voltage(V1,V2)
  L_Analytical
  loss(P1-P2)
L

## Slide 30
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -1 (RANDOM FOREST )
RANDOM FOREST
A TREE
1. Prone To overfitting
2. Poor Generalization

## Slide 31
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -1 (RANDOM FOREST )
Average Error :
0.6%

## Slide 32
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL - 2 (Neural Network)
5 Layers
16 nodes
sigmoid

## Slide 33
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL - 2 (Neural Network)
Average Error :
0.7%

## Slide 34
Power Electronics and Control Engineering (PEACE) Laboratory
6
New architecture
ML MODEL
  Phi
  current(I1,I2)
  Voltage(V1,V2)
  L_Analytical
  loss(P1-P2)
L
Physics
P_Emp
(P_out - P_empherical)

## Slide 35
Power Electronics and Control Engineering (PEACE) Laboratory
6
New architecture
, For Now

## Slide 36
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -1 (RANDOM FOREST +PI )
Average Error :
0.2%
phi only

## Slide 37
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -1 (RANDOM FOREST +PI )
Average Error :
0.6%
phi +del

## Slide 38
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -2 ( PINN )
Average Error :
0.22%
phi only

## Slide 39
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -2 ( PINN )
Average Error :
0.5%
phi +del

## Slide 40
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -2 ( NN )
Average Error :
0.72%
10 values of L

## Slide 41
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -2 ( PINN )
Average Error :
0.71%
10 values of L

## Slide 42
Power Electronics and Control Engineering (PEACE) Laboratory
6
COMPARISON OF MODELS
NN
(5,16,sig)
RF
RF+Physics
PINN
(3,16,sig)
0.6%
Physics uses 1/2 of data
0.6%
0.7%
0.5%
NN(10 L)
(5,32,sig)
0.72%
Average error
PINN(10 L)
(3,32,sig)
0.71%

## Slide 43
Power Electronics and Control Engineering (PEACE) Laboratory
6
PROBLEMS FACED
  Very Slow Training of Model ( 3~ 4hr)
  Ideal Model cant be tuned(nodes,layers,Lambda)
Solution
  Using better systems to train data(Cloud ,Lab PC)
  Re-Code from scratch to make it faster

## Slide 44
Power Electronics and Control Engineering (PEACE) Laboratory
6
FURTHER PLANS
=> Find a better Tuned Model
=> Implement new parameters
=> validate with Hardware data

## Slide 45
Power Electronics and Control Engineering (PEACE) Laboratory
6
ML MODEL
ML MODEL
  Phi,del1,del2
  current(I1,I2)
  Voltage(V1,V2)
  L_Analytical
  loss(P1-P2)
L1
L2
Ron1
Ron2

## Slide 46
Power Electronics and Control Engineering (PEACE) Laboratory
6
PROBLEM
Parameters
  Phi
  del1
  del2
  L1
  L2
  Ron1
  Ron2
10 points per parameter =>10e7 points
Not possible to collect data from Hardware

## Slide 47
Power Electronics and Control Engineering (PEACE) Laboratory
6
SOLUTION
Steps:
  Make a math model
  Collect few Data from hardware
  Tune the model accordingly
  Test on hardware data Again
Make a Math Model that simulates the hardware and generate data from it.

## Slide 48
Power Electronics and Control Engineering (PEACE) Laboratory
6
DATA COLLECTION
Hardware Data
12 points

## Slide 49
Power Electronics and Control Engineering (PEACE) Laboratory
6
DATA GENERATION
Parameters No.
  Phi 9
  del1 8
  del2 8
  L1 6
  L2 6
  Ron1 6
  Ron2 6
720000 data points

## Slide 50
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -1( NN )
Average Error :
25%
26%
22%
41%
4 Layers 16 Nodes

## Slide 51
Power Electronics and Control Engineering (PEACE) Laboratory
6
FEATURE ENGINEERING
Old feature
  Lanalytical
  Power loss
New Features
  cos(del1)
  cos(del2)
  sin(phi)

## Slide 52
Power Electronics and Control Engineering (PEACE) Laboratory
6
FEATURE ENGINEERING
Using Lossless Power equations
at different modes
of operation

## Slide 53
Power Electronics and Control Engineering (PEACE) Laboratory
6
MODEL -1( NN )
Average Error :
20%
19%
19%
38%
4 Layers 32 Nodes

## Slide 54
Power Electronics and Control Engineering (PEACE) Laboratory
6
POSSIBLE REASONS
1. Data closer to actual value ; NN cannot fit it
2. More number of outputs (complex)
3. Large Data for single output i.e Less variation in L
4. stuck at Local Minima

## Slide 55
Power Electronics and Control Engineering (PEACE) Laboratory
6
PINN

## Slide 56
Power Electronics and Control Engineering (PEACE) Laboratory
6
PINN
Implementation Problem
  Default Libraries uses tensors to calculate y_pred
Converted the power func to operate over tensors
2. Converted func cant be integrated with NN
System crashes due to complexity of code/errors
Solution
  code from scratch without libraries
  read tensor documents to integrate

## Slide 57
Power Electronics and Control Engineering (PEACE) Laboratory
6
POSSIBLE SOLUTION
Train Different NN for different outputs
1. L1 and L2
(2 Layer 32 Nodes)
Average Error :
4%
4%
2. Ron1 and Ron2
(3 Layer 64 Nodes)
19%
37%

## Slide 58
Power Electronics and Control Engineering (PEACE) Laboratory
6
POSSIBLE SOLUTION
L1 and L2 (2 Layer 32 Nodes)

## Slide 59
Power Electronics and Control Engineering (PEACE) Laboratory
6
COMPARISION
NN 4 Layers 16 Nodes
Average Error :
25%, 26%, 22%, 41%
NN 4 Layers 32 Nodes
(more features)
Average Error :
20%, 19%, 19%, 38%
L1 and L2 (2 Layer 32 Nodes)
Average Error :
4%, 4%
Ron1 and Ron2 (3 Layer 64 Nodes)
Average Error :
19%, 37%

## Slide 60
Power Electronics and Control Engineering (PEACE) Laboratory
6
FUTURE WORK
  Implement PINN
  Try Genetic Algorithm for best weights
  Implement it on Hardware